## Slide 1: Security Challenges 5G and Beyond Environment
Hypervisor Vulnerability
API security
Orchestration Vulnerability
Virtual monitoring
    Limited visibility to Mobility/EPC interfaces (e.g. S6a, S11, S8)
Virtualized firewalls
Secure boot
Secure crash
User/tenant authentication, authentication and accounting
Topology validation and enforcement
Performance isolation
Authenticated Time Service
Private Keys within Cloud Images
Detection of attacks on resources in virtualization infrastructure
Security monitoring across multiple administrative domains (i.e., Lawful Interception)

## Slide 2: Threat Analysis in 5G Network
Attacks by Mobile End Points (DOS by Flooding)
Attacks with physical access to the transport network
(Man-in-the-middle attack, eavesdropping)
Virtualization Attacks by Third Party VNF
(Side Channel Attacks)
Attacks from physical access to gNodeB
Attacks from untrusted
Non-3GPP network
Insider Attacks
(Data Modification, Data Leakage)
API-based Attacks
Attacks from Internet and other Networks
Compromise of Network Elements
Attacks from
Roaming Network
Theft of Service
Eavesdropping
Attacks on the Radio interface
DOS by jamming

## Slide 3: Mobile Network Security – 5G Core Threat Categories
 | Category | Threat | Description
T1 | Loss of Availability | Flooding an interface | Attackers flood an interface resulting in DoS condition (e.g. multiple authentication failure on N1, N2 interface)
T2 |  | Crashing a network element | Attackers crash a network element by sending malformed packets
T3 | Loss of Confidentiality | Eavesdropping | Attackers eavesdrop on sensitive data on control and bearer plane
T4 |  | Data leakage | Unauthorized access to sensitive data on the server (UDR, UDSF) profile, etc.)
T5 | Loss of Integrity | Traffic modification | Attackers modify information during transit in user plane N3 (SIP header modification, RTP spoofing)
T6 |  | Data modification | Attackers modify data on network element (change the NE configurations through Admin interface)
T7 | Loss of Control | Control the network | Attackers control the network via protocol or implementation flaw
T8 |  | Compromise of network element | Attackers compromise of network element via management interface
T9 | Malicious Insider | Insider attacks | Insiders make data modification on network elements, make unauthorized changes to NE configuration, etc.
T10 | Theft of Service | Service free of charge | Attackers exploits a flaw to use services without being charged

## Slide 4: Key Pillars of 5G and Beyond Security
Optimization / Orchestration Security
Virtualization / Softwarization Security
Edge Security
SDN Security
Predictive Security / Monitoring and Analytics
Cloud RAN Security
5G Core
Edge
Cloud
Network
Slice 1
Network Slice 2
Control Plane
Network Slice 4
vIMS
Data Plane
Cloud RAN
PLMN # 1
PLMN # 2
PLMN # 3
Cloud RAN
Cloud RAN
Supply Chain Security
Open Source / API Security
Network Slicing Security
Data Security and Privacy

## Slide 5: Security Advantages of SDN/NFV A Comprehensive View of SDN/NFV Security Advantages
Streamline and Reduce Patching Cycle Time
Real-Time Integration of “Add-on” Security Functions
Security that Exceeds Existing Perimeter
Streamline and Reduce Incident Response Cycle Time
Centralize Control and Management Functions
Multivendor Security Service
Real-Time Scaling to Absorb DDOS Attacks
Security Embedded at Design Time
Common Hardware (COTS)
Hypervisor
VM
Security Function Vendor 1
VM2
VM3
Orchestration
SDN
VM1’
VM1
SDN Controller
SLA Mgmt
Analytics
Usage Mgt
Monitoring
Data Analytics
VM1’’
VM2’
VM2’’
VM3’
VM3’’
VM
Security Function Vendor 2
VM
Security Function Vendor 3
Design Enhancements:
Real-Time capabilities:
Performance Improvements:

## Slide 6: An Example - Security Transformation – Virtual Firewall/Virtual DDOS/Virtual IPS
Virtualized Security Function
Infrastructure Controller
Network Controller
Application
Controller
Operational Management Framework
Common Cloud Infrastructure
Non-Virtualized Security
Wide variety of vendor specific security hardware
Requires vendor specific FW management platforms
Requires hands-on customized physical work to install
Multiple support organizations
No single operations model or database of record
Security functions will be cloud-based
Security dynamically orchestrated in the cloud as needed
Streamlined supplier integration
Centralized common management platform
Creates a standard operations/support model
Virtual Security Functions
vFW1
vFW2
vDDOs
IDS1
IDS2
GUAVUS
paloalto
networks
Intel
Security
FORTINET
Alcatel-Lucent
HP
ARBOR
NETWORKS
NETSCOUT
A10 NETWORKS
f5
radware
ALLOT
sandvine
m o v i k
JUNIPER
NETWORKS
NIKSUN
Check Point
FireEye
Tektronix

## Slide 7: Security-As-a-Service Proposed Approach with Dynamic Service Chaining – An Opportunity Use Case - Malware Mitigation
Data Plane
Control Plane

## Slide 8: Security Opportunities from Virtualization DDoS Attack Resiliency – Control Plane
Common Hardware (COTS)
Hypervisor
vS-GW
vP-GW
vHSS
vPCRF
vPCEF
Orchestration
SDN
SGi
S1-U
S1-MME
Attacker creates a Botnet army by infecting many Mobile devices with a ‘remote-reboot’ malware, attacker then instructs the malware to reboot all the devices at the same time, this will cause excessive malicious Attach Requests, creating a Malicious Signaling Storm.
vMME is under DDoS attack
Orchestrator instantiates new VM to scale-out vMME function to sustain the higher traffic load while we investigate.
vMME
vMME
3
2
1

## Slide 9: Security Opportunities from Virtualization SDN Controller Dynamic Security Control – Data Plane
Customer Cloud Services
SDN
SGi
S1-U
S1-MME
SDN Controller
vFirewalls
vRouters
Malware on Mobile Devices sends malformed IP packets directed to a Customer Cloud Services
SDN Controller dynamically modifies the firewall rules for the related firewalls to thwart the attack
Non-malicious traffic
Network Intelligence Layer
3
2
1

## Slide 10: Cloud RAN Security

## Slide 11: Example: CLOUD RAN Unique 5G Security Opportunities, Challenges, and Mitigation
5G Capabilities | Potential Security Challenges | Potential Mitigation
The 5G networks will facilitate many more devices (IoT) accessing the RAN with shared access. Programmability and Virtualization of RAN will adapt to dynamic nature of traffic and multi provider access | Huge number of infected M2M/IOT devices that attempt to gain access resulting in shared resource starvation, VM/Guest OS manipulation, data exfiltration | Hypervisor Separation Intelligent VM resource allocations vFirewalls
 | Programmable and Software RAN will increase the chance of Man-In-The-Middle Attack at the base station | Use of analytical techniques like anomaly detection can be leveraged for such analysis
 | Resource starvation at cRAN VNFs by additional vFirewall functions during DDOS attack | Hypervisor separation Capping of resources
 | External flooding attacks may be launched by a botnet consisting of large number of bots and Distributed Denial of Service (DDoS) | Develop DDoS detection and mitigation functions into Cloud RAN functions
 | Jamming can be launched against control-plane signaling or user-plane data messages | Deploy DDOS detection, IDS and vFirewall functions Dynamic Service Chaining
Potential Security Opportunities/Benefits |  | 
SoftRAN (cRAN) in 5G networks will have embedded DoS detection and mitigation functions Dynamic Radio Resource Scheduling would significantly reduce the risk of jamming attacks targeting mission critical devices Access to control plane and media plane at the base station will enable security monitoring of traffic |  |